## Slide 1: Unit II Shear Force and Bending Moment Diagrams
CO2. DRAW Shear force and bending moment diagram for various types of transverse loading and support.
SFD & BMD: Introduction to SFD, BMD with application, SFD & BMD for statically determinate beam due to concentrated load, uniformly distributed load, uniformly varying load, couple and combined loading, Relationship between rate of loading, shear force and bending moment, Concept of zero shear force, Maximum bending moment, point of contra-flexure

## Slide 2: Types of Beams

## Slide 3: Types of Loads

## Slide 4: Shear Force Diagram (SFD)
A shear force (SF) is defined as the algebraic sum of all the vertical forces, either to the left or to the right hand side of the section
Shear Force Diagram: is graph connecting Shear Forces at various locations on the beam.
A shear force which tends to rotate the beam in clockwise direction is positive and vice versa

## Slide 5: Bending Moment Diagram (BMD)
A bending moment (BM) is defined as the algebraic sum of the moments of all the forces either to the left or to the right of a section.
BMD: Diagram is graph connecting bending moments at various locations

## Slide 6: General Guidelines on Construction of SFD and BMD
The load, shear and bending moment diagrams should be constructed one below the other, in that order, all with the same horizontal scale.
The dimension on the beam need not be scaled but should be relative and proportionate
Ordinates (i.e., BM and SF values) need not be plotted to scale but should be relative. Curvature may need to be exaggerated for clarity.
Principal ordinates (BM and SF values at salient points) should be labeled on both SFD and BMD.
7

## Slide 25: Sign Conventions for the Bending Moment:
a) Positive Bending Moment (Sagging)

## Slide 26: b) Negative Bending Moment(Hogging)

## Slide 27: Point of Contraflexure:
It corresponds to a point where the bending moment changes the sign, hence in order to find the point of contraflexures obviously the B.M would change its sign when it cuts the X-axis therefore to get the points of contraflexure equate the bending moment equation equal to zero. The fibre stress is zero at such sections

## Slide 39
Interpretations |  |  |  | 
 | Types of Loading | Shape of Shear Force Diagram | Shape of Bending Moment Diagram | 
 | Point Load | Sudden Jump at load and constant at other locations | Linearly Varying Graph (Straight Line) | 
 | Uniformly Distributed Load (UDL) | Linearly Varying Graph (Straight Line) | Parabolic Graph (Smooth Curve) | 
 | Uniformly Varying Load (UDL) | Parabolic Graph (Smooth Curve) | Cubically varying Graph (Curve) | 
 | Moment Couple | No effect | Sudden Jump at Moment and constant at other locations 40 | 

## Slide 40: Relationship between shear force, bending moment
41